## Slide 1
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
loop unrolling
code
worst-case execution
real-time software
predication
time
Sokratis Koseoglou

## Slide 2
Loop Unrolling-Code Predication
Motivational Example
Authors’ Optimization Approach
Evaluation & Results

## Slide 3
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Worst-Case Execution Time (WCET)
Worst-Case Execution Time (WCET) is an important parameter for a Real-Time System
Time Analyzers are used in order to evaluate the WCET
There are two ways to reduce the WCET
Faster Processor
Software Optimization
Goal of this paper is to reduce the WCET of a real-time system
1

## Slide 4
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Loop Unrolling
for(int i = 10; i != 0; i = i - 1){
a[i] = a[i] + b;
}
for(int i = 10; i != 0; i = i - 2){
a[i] = a[i] + b;
}
LOOP: LW r2, 0(r1)
ADD r2, r2, r3
SW r2, 0(r1)
ADDI r1, r1, -4
BNE r1, r5, LOOP
LOOP: LW r2, 0(r1)
ADD r2, r2, r3
SW r2, 0(r1)
LW r2, -4(r1)
ADD r2, r2, r3
SW r2, -4(r1)
ADDI r1, r1, -8
BNE r1, r5, LOOP
Loop Unrolling
Unrolling Factor = 1
5 Instr. x 10 Iter. = 50 Instructions
8 Instr. x 5 Iter. = 40 Instructions
2
a[i - 1] = a[i - 1] + b
Loops are frequently good targets for compiler optimizations

## Slide 5
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Loop Unrolling – keil μVision ARM Example
3
Demo Code for Loop Unrolling
Rolled Loop Time
Unrolled Loop Time

## Slide 6
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Branch Prediction vs Code Predication
If (f){
a++;
}else{
a--;
}
Branch Prediction
Code Predication
Predict whether a branch is taken or not
Synchronous Architectures have about 90% Accuracy
No penalty if correct prediction
Huge penalty if wrong prediction
Do work of both directions
Waste up to 50%
Throw away instructions from the wrong path
Big if-else
Small if-else
Branch Prediction
Code Predication
ADDI r2,r2,1
(not f) ADDI r2,r2,-1
BEQ r1, 0, else
ADDI r2,r2,1
else:
ADDI r2,r2,-1
4

## Slide 7
Loop Unrolling-Code Predication
Motivational Example

## Slide 8
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Motivational Example Loop
Data-Dependent Loop (since loop iterations variable is not static)
Compiler generated a Control Flow Graph (CFG)
A problem with Data-Dependent loops is the difficulty to choose an effective unrolling factor
We need to add exit conditions for each body replication
for(i = 0; i < a; i++)
j++;
k++;
(Header)
(Body)
5

## Slide 9
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
6
Loop Unrolling – keil μVision ARM Example
Demo Code for Loop Unrolling with exit conditions

## Slide 10
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Note that, instructions increased
If the target architecture supports code predication, we can consider the following code, in which we are able to do if-conversion
Motivational Example Loop
7

## Slide 11
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Motivational Example Loop
The prefix (p) means that the execution of blocks body2 and body3 are conditioned to some predication guard p
8

## Slide 12
Loop Unrolling-Code Predication
Motivational Example
Authors’ Optimization Approach

## Slide 13
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Predicated Loop Unrolling Algorithm
Identify Header & Body of the loop
Remove unconditional branch and place it in the end
Create a body copy which will be always executed
Create predicated body copies inside the for loop, with U iterations, where U is the unrolling factor
9

## Slide 14
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Example of our Approach
Assembly
10

## Slide 15
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
11
Example of our Approach
Standard Approach with branch for exit conditions
Predicated Approach
We can see that the predicated version has fewer instructions

## Slide 16
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Optimization Choice Algorithm
Standard (without branches)
Used for non-data dependent loops (with fixed executions counts)
Standard (with branches)
Used for data dependent loops that have call instructions in the body
Predicated
Used for data dependent loops that have simple bodies and do not use call instructions
Optimizations Algorithm that is executed by the compiler
Compiler runs this code for each loop that is in the WCEP
12

## Slide 17
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Unrolling Factor Selection
13
It is necessary to find the optimal Unrolling Factor for each loop that resides inside the WCEP
If it is in the WCEP, we test different Unrolling Factors, from 2 to 17
For Data-Independent loops the Unrolling Factor must exactly divide the execution count of the loop in order to avoid corner exit conditions
For Data-Dependent loops we consider Unrolling Factors whose parity is equal to the loop bounds’ parity
Then we recompile the program and test for WCET changes
Algorithm complexity is O()
Better WCET with the cost of higher compilation time

## Slide 18
Loop Unrolling-Code Predication
Motivational Example
Evaluation & Results
Authors’ Optimization Approach

## Slide 19
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Target Architecture
14
Supports a simplified complete Predication Support
32-bit Microprocessor with RISC Instructions
Direct-Mapped Cache Memory(32 blocks of 256 bits, thus 1024kB)
No Data-Cache
No out-of-order execution
Four issue, five stage static scheduled pipeline

## Slide 20
Combining loop unrolling strategies and code predication to reduce the worst-case execution time of real-time software
Results
15
A total of 18 from 33 benchmarks are shown, since there was no gain in the other ones
We can see that the combination of techniques was able to reduce the WCET of half of the benchmarks

## Slide 21
Thank you for your time!
Questions?